## Slide 1
Welcome
Load-Shedding Stage Forecasting
Using LSTM Time-Series Classification
Thebe Ledwaba · Precious Skosana
EIARI4A | Final Year Project

## Slide 2
OVERVIEW
Agenda
01
Problem & Objectives
02
Dataset & Features
03
Distribution Shift
04
Methodology
05
Hyperparameter Tuning
06
Results
07
Why Persistence Won
08
Limitations & Future Work
09
Conclusion

## Slide 3
PROBLEM STATEMENT
Problem & Objectives
THE PROBLEM
Load-shedding alerts show current stage — not future stages
No public forecasting tool exists
By the time you know, it's too late to prepare
SUCCESS TARGETS
MAE
< 0.7
Mean Absolute Error
RMSE
< 1.0
Root Mean Square Error
LSTM
+15%
Better than baseline

## Slide 4
DATA
Dataset & Features
ESK2033
Eskom Hourly Grid Metrics
43,000+
rows
EskomSePush
Stage History (resampled)
Hourly
forward fill
ENGINEERED FEATURES
Lag 1h / 24h / 48h
Sin/Cos Hour Encoding
Sin/Cos Day Encoding
Sin/Cos Month Encoding
12h Rolling Stats
5 Eskom Grid Metrics
Window: 24 hours

## Slide 5
KEY FINDING
Stage Distribution Shift
The single biggest reason our LSTM struggled
TRAINING 2018–2021
Dominant Stage
Stage 0
~80% of hours
Stages 3–6 barely existed
TEST 2022–2023
Dominant Stage
Stage 4
34% of hours
Non-zero stages. Stage 4: 750 hrs. Stage 6: 300+ hrs.
VS
Note: This analysis contextualises future deployment risk — primary evaluation was conducted on the March–July 2022 test set.

## Slide 6
APPROACH
Methodology — Three Models
01
Persistence
Baseline
Next hour = current hour
Strong during stable periods
02
Logistic
Regression
Multiclass + class weights
Same 16 engineered features
03
Stacked
LSTM
2 LSTM layers + dropout
Softmax output, cross-entropy loss
Train: 2020–2021
Validation: 2021–2022
Test: 2022–2023

## Slide 7
OPTIMISATION
Hyperparameter Tuning
12
Combinations
Tested
3
Fold
TimeSeriesSplit
128
Best
LSTM Units
0.001
Best
Learning Rate
BEST CONFIGURATION
128 Units · 0.2 Dropout · Learning Rate 0.001 · Saved in tuning_log.csv

## Slide 8
PERFORMANCE
Results — March–July 2022 Test Set
WINNER
Persistence
Baseline
RMSE
0.658
ACCURACY
91.5%
2nd
Logistic
Regression
RMSE
0.973
ACCURACY
72.0%
3rd
Stacked
LSTM
RMSE
1.398
ACCURACY
52.0%
⚠ LSTM: 0% recall on Stages 3–6 · 112% worse than persistence

## Slide 9
ANALYSIS
Why Persistence Won
01
Distribution Shift
Trained on 2018–2021 (Stage 0 world) · Tested on 2023 (Stage 4 world)
02
Too Few High-Stage Examples
Only 52 Stage 3 · 77 Stage 4 · 0 Stage 5 training examples — can't learn what it never saw
03
2023 Was a Chronic Crisis
Stages persisted for days — 'same as last hour' is almost always right
The LSTM wasn't wrong — it was unprepared for a test period that looked nothing like its training data.

## Slide 10
REFLECTION
Limitations
These were my design choices — not limitations of LSTMs in general.
01
Training data: 2018–2021 only
Should have used 2022–2024 data with real crisis patterns
02
Fixed 24-hour window
Other window sizes and dynamic windows were not explored
03
No exogenous variables
Weather data, maintenance schedules, holiday calendar all influence real decisions

## Slide 11
NEXT STEPS
Future Work
P1
Retrain on 2022–2024 data
Balanced Stage 4–6 examples — this single change could flip the results
P2
Hybrid model
Persistence during stable periods · LSTM only when transition is likely
P3
Add exogenous features
Temperature, winter flags, public holidays for better context
P4
Hierarchical classification
First predict: will load-shedding happen? Then: which stage?

## Slide 12
End
Thank you for listening!
Thebe Ledwaba · Precious Skosana | EIARI4A Final Project